## Slide 1: KANDAVAS LAUKSAIMNIECĪBAS TEHNIKUMS
LAUKSAIMNIECĪBAS MEHANIZĀCIJAS TEHNIĶIS LAUKSAIMNIECĪBAS MEHANIZĀCIJAS TEHNIĶIS «LAUKSAIMNIECĪBAS TEHNIKAS UN IEKĀRTAS TA» «COMMON RAIL (CR) IESMIDZINĀŠANAS SISTĒMA UN DEVĒJU PĀRBAUDE»
I.Ešenbergs
08.01.2026

## Slide 2
«COMMON RAIL (CR) IESMIDZINĀŠANAS SISTĒMA UN DEVĒJU PĀRBAUDE»

## Slide 3
B00. Engine designation
Engine designation according to model
4 valve/cylinder engine
T: Turbocharger
S: Intercooler
D: Fast Diesel engine
4.1/6.1: Displacement:
L: In-line
6: 6 cylinders
SCR: Urea injection emissions control system
BRAND | ENGINE TYPE
Deutz-Fahr, 6160, 6180, 6190 TTV7210,7230,7250 | TCD 6.1 L4 SCR
Lamborghini MACH 210, 230, 250 | TCD 6.1 L4 SCR
Significance of nomenclature used in engine type TCD 6.1 SCR (example)

## Slide 4
B00. Location of engine identification plates
KEY:
C = Engine identification plate
D = Stamped engine serial number
Engine identification plate

## Slide 5
B00. Identification plate
Information on engine identification plate

## Slide 6
B00. View of the engine
Right hand side view of engine TCD 6.1 L6 SCR
Aspirated air inlet
Alternator
Poly-V belt
Coolant inlet
Engine oil filter
Oil sump
Engine oil cooler
Fuel filter
Rail
Oil filler cap
Bleed screw

## Slide 7
B00. View of the engine
Left hand side view of engine TCD 6.1 L6 SCR
Aspirated air inlet
Coolant outlet
Turbocharger outlet (exhaust)
Engine oil filler neck
Engine oil dipstick

## Slide 8
B06. Lubrication circuit
1. Oil sump
2. Oil pickup line
3. Oil cooler
4. Check valve
5. Radiator bypass
6. Filter bypass
7. Pressure cut-off valve
8. Filter
9. Primary line
10. Piston cooling nozzle
11. Rocker
12. Turbocharger
13. Compressor and/or hydraulic pump

## Slide 9
B07. The Deutz engine and emissions compliance
Diagram of emissions regulations
The diagram above illustrates the engine emissions limits permitted by different tiers of emissions regulations in a simplified format.
Note that while tiers COM II and COM III permit the same level of particulate emissions.
the lower limit for NOx emissions requires a reduction from approximately 6 g/kWh to approximately 4 g/kWh.
Over the next 15 years, the particular and NOx emissions produced by Diesel engines must be reduced by over 96% and over 95% respectively.

## Slide 10
B07. The Deutz engine and emissions compliance
Possible technical solutions
- Compliance with COM II regulations is achieved by modifying injection rates while maintaining high injection pressures.
Compliance with COM III regulations for NOx emissions is only possible with exhaust gas recirculation.
- To achieve compliance with IIIB regulations, a selective catalytic reduction system with urea injection is used. This solution makes it possible to eliminate the exhaust gas recirculation system.
Reducing NOx emissions:
NOx emissions are reduced with an after-treatment system. Urea (AdBlue) is injected into the exhaust gases before they are passed through a catalytic converter. The reaction catalysed on contact with the surface of the catalytic converter breaks NOx compounds down into H2O and N2. The SCR system is used to eliminate the NOx compounds produced during combustion.
Reduction of particulate, HC and CO emissions:
Particulate, HC and CO emissions are reduced by higher combustion temperatures, made possible by the use of urea injection to reduce NOx emissions. High combustion temperatures reduce HC and CO emissions and also reduce consumption
NOx
Particulate
"Cold combustion"
"Hot combustion"
Tier4i
Stage IIIB
Euro I, Tier I
Optimisation of combustion with EGR
Euro IIIa
Tier 3
DPF
SCR
EGR injection
Higher engine temp.
High pressure injection

## Slide 11
B07. Operating principle of Deutz Common Rail system
ECU
10 µm pre-filter with water separator
Manual pump
Fuel pump
Main filter (2 µm)
HP pumps
Injectors
DBV
Rail
FCU
Pressure sensor
2
2
3
3
2
3
p
= 0 to 0.5 Bar
p
= 300 to 1,600 Bar
p
= -0.3 to 0 Bar
p
= 6 Bar (+/- 1 Bar)
ECU: Electronic Control Unit
FCU: Fuel Control Unit
DBV:
Pressure cut-off valve
Pressure sensor
MProp
(FCU)
The fuel in the tank is aspirated by the fuel pump.
A manual pump ahead of the fuel pump makes it possible to prime the circuit when necessary, such as after replacement of the filter.
A fuel pre-filter is situated after the pump. This filter removes the coarser particles contained in the fuel (15 microns). Water is also separated to keep it out of the high pressure circuit.
The main fuel filter, with a filtration capacity of 5 microns, is situated after the fuel pump.
The fuel pressure is monitored by a pressure sensor, which sends the relative pressure signal directly to the ECU.
Common Rail system layout

## Slide 12
The fuel is now fed into the FCU valve. This valve dispenses the precise quantity of fuel necessary for engine operation. The FCU valve is piloted directly by the ECU. This means that the high pressure pumps receive only the precise quantity of fuel that the system effectively needs.
The two high pressure pumps are driven by the camshaft. These pumps deliver fuel to and pressurise the rail (raising pressure from 400 to approximately 1,600 bar).
The rail constitutes the high pressure reservoir of the system, and is connected directly to the injectors. A sensor monitors the pressure in the rail and sends the relative pressure signal to the ECU. A pressure limiting valve, calibrated to open at 1,800 bar, is also installed on the rail.
The injectors deliver the necessary quantity of fuel into the combustion chambers. The aperture and closure of the injectors are controlled electrically by the ECU. The injectors are opened multiple times during a single combustion cycle to produce the required torque and reduce the exhaust emissions produced by the engine.
A number of other sensors are installed in the engine to monitor the functions of the engine itself. These sensors are connected to the ECU.
B07. Operating principle of Deutz Common Rail system
Common Rail system layout

## Slide 13
1,600 bar circuit
B07. Operating principle of Deutz Common Rail system
Rail
a
Tank
FCU 3
PF45-16
Fuel pump
Injectors
max. 70 °C
Pre-filter with water separator
Main filter with pressure sensor
Rail pressure sensor
DBV
6 bar
max. +0.5 bar
Control unit
EDC 17
Steuer
-
gerät
CRIN3.3-20 Injectors
Rail
a
Tank
max. 70 °C
Rail
a
PF45-20
FCU 3.1
Auxiliary return line
Main filter with pressure sensor
Rail pressure sensor
DBV
Fuel pump
ECU EDC 17
6 bar
max. +0.5 bar
Pre-filter with water separator
2,000 bar circuit
Common Rail system layout

## Slide 14
B07. Operating principle of Deutz Common Rail system
The following diagram illustrates the positions on the engine of the main elements of the fuel injection circuit.
Fuel tank
Fuel pre-filter
Fuel pump
Fuel filter
FCU valve feed
FCU valve
High pressure pump
Rail
Injector
Return line to tank
Return line (2,000 bar system)

## Slide 15
B07. Low pressure circuit
The fuel pump.
TCD 6.1
Characteristics of the fuel pump
(back pressure back p = 6 bar)
0
1
2
3
4
5
6
0
500
1,000
1,500
2,000
2,500
3,000
3,500
4,000
4,500
5,000
5,500
6,000
6,500
7,000
Pump speed (pump n) in rpm
Flow capacity [l/min]
The fuel pump aspirates fuel from the tank via the pre-filter and delivers fuel to the FCU.
The pressure ahead of the pump must be between -0.3 and 0 Bar, while the pressure after of the pump must be approximately 6 Bar.
p
[bar]
n
Engine
[rpm]
Q [L/min]
3
100
0.333
10
1,000
1.83
10
2,300
2.92

## Slide 16
B07. High pressure circuit
Overview
1
2
3
4
5
6
7
8
9
10
FCU valve
FCU outlet to HP pumps
HP pump
HP pump outlet to rail
Rail
Line to injector
Return line from rail via pressure limiter
Return line from injectors
Return line from FCU valve
To tank

## Slide 17
FCU valve
The FCU valve, controlled by the ECU unit, delivers the necessary quantity of fuel to the pumps in relation to engine speed and engine load.
This pressurises the rail.
The FCU valve contains a proportional solenoid valve powered with PWM current.
There are two different types of FCU valve, 3.0 and 3.1. The type used depends on the injection system.
B07. High pressure circuit
Feed to
Return line
FCU Version 3 (left hand view)  CRSN 2, 1600 bar
FCU Version 3.1 (right hand view)  CRSN 3.3, 2000 bar
To HP pumps
To fuel pump
What is the difference between the FCU 3.0 and FCU 3.1?
The FCU 3.1 has an auxiliary return line from the 2,000 Bar system.
The auxiliary return line of the FCU 3.1 (from 2,000 Bar system only) is connected to the fuel pump inlet and is used to produce a negative pressure (vacuum).
This is necessary due to the seal tightness of the injectors when closed, and is the only solution possible for producing a return pressure of 0 to 0.5 Bar in the return circuit. If there were no auxiliary return line, excessively high pressures would develop in the system.
An auxiliary return line is not necessary in the 1,600 Bar system as the injectors deliver fuel continuously.
IMPORTANT:
While the FCU 3.0 and FCU 3.1 are similar in appearance, they not interchangeable! Risk of engine damage

## Slide 18
FCU valve 3.0
- CRNS 2 injectors, 1,600 Bar
B07. High pressure circuit
1
2
3
Feed to
To HP pumps PF45-xx
Return line
ÜV- flow rate regulator valve Pmax: 6 bar
Zero flow drain line
M-Prop
Delivery </= 8 Bar
To HP pumps
Return </= 0.5 Bar
Zero flow drain line, 0.4 mm diam.

## Slide 19
FCU valve 3.1
- CRNS 3.3 injectors, 2,000 Bar
B07. High pressure circuit
1
2
3
4
Feed to
To HP pumps PF45-xx
Return line to tank
To fuel pump
ÜV- Relief valve Pmax: 6 Bar
Zero flow drain line
M-Prop
Degassing orifice 0.4 mm diam.
Zero flow restrictor, 0.4 mm diam.
To HP pumps
Return to tank </= 0.5 Bar
Delivery, </= 8 Bar
Return to fuel pump </= 200 mbar

## Slide 20
1. Solenoid valve
2. Core
3. LP pump feed
4. To HP pumps
5. LP pump feed
When the FCU is not electrically powered, the valve shutter (orange) is held back by the spring at the base of the shutter itself.
In this state, the valve is 100% open and large quantities of fuel received from the fuel pump passes through the valve to the HP pumps.
When the valve is electrically powered, the shutter closes, permitting only a part of the fuel delivered to pass through to the HP pumps. This quantity is metered by varying the PWM current energising the FCU valve.
When the valve is completely closed, the HP pumps receive no fuel. In this state, fuel received from the fuel pump is sent back to the return line.
FCU valve
B07. High pressure circuit

## Slide 21
High pressure pump
B07. High pressure circuit
The two high pressure pumps feed the rail with fuel.
Two conditions must be met for fuel to be delivered correctly to the rail.
- There must be no communication between the rail and the pump during the descending stroke of the pump piston ("aspiration" stroke)
- There must be a pressure of at least 1.7 Bar to feed the HP pumps correctly
There are two types of pump:
- PF45-16: CRSN 2, 1,600 Bar
- PF45-20: CRSN 3.3, 2,000 Bar
The two pumps are identical externally. Installing pump PF 45-16 instead of pump PF 45-20 may cause engine damage. Installing PF 45-20 instead of PF 45-16 may cause malfunction
The two high pressure pumps are driven by the camshaft.
Each pump has 3 cams.
The cams are offset by 60° relative to one another.
This ensures that the rail is filled at each injection system, for optimum pressure stability in the rail.
The two pumps (PF 45-16 and PF 45-20) differ in the stroke of the piston (10 and 12 mm).
To rail
Feed to
Check valve
Tappet

## Slide 22
Rail
B07. High pressure circuit
The rail protects the system and acts as a high pressure injection reservoir.
The TCD 6.1 L6 engine may be fitted with two different types of rail, depending on the desired operating pressure for the system.
- CRSN 2
- max. operating pressure 1,600 Bar,
- valve aperture pressure 1,850 Bar.
- CRSN 3.3
- max. operating pressure 2,000 Bar,
- valve aperture pressure 2,650 Bar.

## Slide 23
Injectors
B07. High pressure circuit
Two different types of injector may be installed in Deutz TCD SCR engines.
Fuel is delivered via an 'internal' line, with a line inside the head connecting the injector with the rail.
The resistance measured between the two contacts of the injector is approximately 0.5 ohm.
Injector for 4-valve engines
The two types of injector available are:
CRIN2
 CRSN2, 1,600 Bar
CRIN3.3  CRSN3.3, 2000 Bar
(when the engine is switched off, the pressure in the rail is released by forcing the injectors open and holding them open for a few seconds, which produces a very loud whistling/buzzing noise)
Model:
With CRIN 2 and CRIN 3.3 injectors, a filter is installed in the pressurised line
Important:
Observe the correct torque when tightening the terminals of the injectors to prevent electrical damage to the injectors themselves. Do not exceed 1.5 Nm.

## Slide 24
Injectors
B07. High pressure circuit
Operating principle
The fuel reaches the injector (4) at high pressure, and flows through the restriction (9) the base of the injector, to fill the chamber (8).
The rail pressure is the same on both sides of the injector actuator rod (10).
An additional 50 N spring prevents the roller from moving while the pressure is too low.
The excitation current (approx. 20 A) acts on the armature (5) and overcomes the force of the spring (2).
The high current causes the injector needle to lift rapidly.
The solenoid valve lifts the sphere (6) (0.26 mm), causing the pressure in the actuating chamber (8) to drop.
Once at maximum injector needle travel (approx. 50 µm), 0.3 ms after excitation of the solenoid valve, the current drops to approximately 12A, which is sufficient to keep the injector open.
U = 12 V

## Slide 25
B07. High pressure circuit
Injectors
CRIN 3.3 (2,000 Bar) injectors differ from CRIN 2 units in a number of aspects, among which the fact that they are assigned an IQA (Injector Quantity Adjustment) code. This code is used to adjust the flow rate of the injector in relation to a reference table, and makes it possible to adjust injection times in relation to the specific characteristics of the injector.
The injector has two different markings:
- G: Assembly letter (used only for the assembly line)
- 6IAHS6A61A: IQA code
The code for each injector must be entered in the engine control unit memory. On the production line, the IQA codes are entered directly in the engine dataset.
In the event of replacement of an injector, the code of the new injector must be entered using SERDIA 2010. Replacing an injector without entering the IQA code is not permitted.
After replacing an EDC 17 ECU programmed with the original dataset, the IQA codes must also be entered (if any injectors have been replaced).
Entering IQA codes
Recording IQA values
Entering codes into Serdia 2010
Transferring values to ECU

## Slide 26
Injector calibration
IMA code (2,000 Bar)
Entering IQA codes
Recording IQA values
Entering codes into Serdia 2010
Transferring values to ECU
On assembly line
The injector codes are entered in the dataset.
Replacing an injector
After replacement, the code of the new injector must be entered using Serdia 2010. Replacing an injector without entering the respective code is not permitted.
After replacing an EDC ECU programmed with the original dataset, the IQA codes must also be entered (if any injectors have been replaced).
B07. High pressure circuit

## Slide 27
B07. High pressure circuit
Injectors
ZFL (Zero Fuel calibration during Low idle) = injector calibration at zero-load idle speed (for 2,000 Bar system only)
Purpose:
The purpose of ZFL calibration is to compensate for injector wear. With increased wear, the injection time increases to such an extent that injection becomes perceptible to the crankshaft speed sensor. Performing this procedure adapts the injection time accordingly. ZFL has no influence on engine performance. Failure to perform ZFL calibration may result in excessive engine noise.
Required conditions:
ZFL calibration is launched automatically as soon as the following conditions are met:
    Engine speed = idle, zero load
    Coolant temperature = between 65 and 100 °C
    Aspirated air temperature > 0 °C
    no variation in engine load
The procedure is conducted at different rail pressure values (500, 900 and 1300 Bar). An interval of 30 minutes is allowed to elapse between each calibration run. The interval is interrupted if the ECU is switched off. The calibration run for each rail pressure value takes 5 minutes. Data is memorised only when the ECU is powered.
Important:
In the event of injector replacement, the values stored in the dataset must be re-initialised using the SERDIA 2010 (UseCase - operating hours). The engine must then be run at operating temperature at idle speed and with zero load until the new injectors have been calibrated with the ZFL procedure.

## Slide 28
Injectors
B07. High pressure circuit
The quantity of fuel injected depends on two parameters:
- The injector aperture time
- The injector feed pressure
The longer the injector aperture time, the greater the quantity of fuel injected.
However, it is not physically possible to increase injections times, which must be brief to ensure correct engine operation and low emissions.
This means that the injection pressure must also be modified in order to increase or decrease the flow rate of injected fuel.
The following graph shows the relationship between injector aperture time, rail pressure and quantity of fuel injected.

## Slide 29
Injectors
B07. High pressure circuit
3 injection pulses are performed for each engine cycle,
1. Pre-injection
2. Main injection
3. Post-injection
These 3 injection pulses are performed within a time period of approximately 4 ms.
pre-injection:
Prepares the combustion chamber for the main injection pulse:
- pressure and temperature;
- shortening the ignition time for the main injection pulse;
- optimising combustion
This reduces: - combustion noise;
- hydrocarbons emissions;
- fuel consumption.
Results of post-injection:
- reduced NOx emissions;
- reducing fuel consumption.
3
1a. Pressure increase with pre-injection
2a. Pressure increase without pre-injection

## Slide 30
B09. Cooling circuit
Engine coolant radiator
Coolant inlet
Water pump
Partial coolant bypass for oil radiator
Engine oil cooler
Coolant delivery to engine
Upper engine cooling circuit
To cab heater
Heat exchanger
Return line from cab
Thermostat feed line
Return line from radiator
from expansion tank
to expansion tank
Engine cooling

## Slide 31
B08. Testing sensors
Location of sensors
6. Central connectors
7. Crankshaft speed sensor
8. Rail pressure sensor
9. Lubricant oil pressure sensor
10. Oil level sensor (optional)
11. Camshaft speed sensor
      Intake air pressure and temperature sensor (TCD 6.1L6)
  Low fuel pressure sensor
Coolant temperature sensor
Intake air pressure and temperature sensor (TCD 4.1L4)
Engine ECU

## Slide 32
Coolant temperature sensor
Pin measured to test sensor |  |  |  | 
ECU cv52 | ECU cv56b | Connector X 17 | Sensor | Function
D2.1.35 | D2.2.57 | 27 | 1 | Ground
D2.1.13 | D2.2.28 | 24 | 2 | Signal
B08. Testing sensors

## Slide 33
The engine will start in this state.
Example alarm produced by disconnecting engine coolant temperature sensor.
Alarm code on Infocenter / WOD:
Alarm code in Serdia 2010 diagnostic system
B07 Electrical components
Engine alarm:
SPN 110 FMI 3

## Slide 34
Coolant level sensor
Pin measured to test sensor |  |  |  |  | 
ECU cv52 | Connector MS1 cv52 | ECU cv56b | Connector MS1 cv56 | Sensor | Function
D2.2.62 | B5 | D2.1.13 | B5 | 1 | Power
 |  |  |  | 2 | Ground
D2.2.57 | B6 | D2.1.29 | B6 | 3 | Signal
1 = 12 V power feed
3 = Signal
2 = Ground
Coolant level
Voltage measured
Level OK
Level OK
Level too low
U max.
U low signal
U high signal
Interval 7 s
B08. Testing sensors

## Slide 35
The engine will start in this state.
Example alarm produced by disconnecting low coolant level sensor.
Alarm code on Infocenter / WOD:
Alarm code in Serdia 2010 diagnostic system
B07 Electrical components
Engine alarm:
Coolant level

## Slide 36
Aspirated air pressure and temperature sensor
Pin measured to test sensor |  |  |  | 
ECU cv52 | ECU cv56b | Connector X 17 | Sensor | Function
D2.1.74 | D2.1.42 | 28 | 1 | Ground
D2.1.11 | D2.1.27 | 29 | 2 | Temperature signal
D2.1.21 | D2.1.24 | 22 | 3 | Power feed (5 VDC)
D2.1.73 | D2.1.43 | 23 | 4 | Pressure signal
Relative turbocharger pressure in Bar | Signal in volts
0 | approx. 1.0
0.5 | approx. 1.55
1.0 | approx. 2.1
max. 1.6 | approx. 2.7
Temperature values |  | 
Temperature in °C | Temperature in °F | Resistance in ohms
- 40 | - 40 | 44.373K
0 | 32 | 5,774
25 | 77 | 2,014
40 | 104 | 1,150
80 | 176 | 315
125 | 257 | 98
B08. Testing sensors

## Slide 37
The engine will start in this state.
Example alarm produced by disconnecting turbo temperature and pressure sensor.
Alarm code on Infocenter / WOD:
Alarm code in Serdia 2010 diagnostic system
B07 Electrical components
Engine alarm:
Turbo pressure/Intake manifold air temp.

## Slide 38
Low fuel pressure sensor
Pin measured to test sensor |  |  |  | 
ECU 52 | ECU 56b | X 17 | Sensor | Function
D2.1.21 | D2.1.24 | 23 | 1 | Power feed (5 VDC)
D2.1.54 | D2.1.85 | 17 | 2 | Signal
D2.1.35 | D2.1.57 | 27 | 4 | Ground
Low fuel pressure sensor
2
4
1
3
B08. Testing sensors

## Slide 39
The engine will start in this state.
Example alarm produced by disconnecting low fuel pressure sensor.
Alarm code on Infocenter / WOD:
Alarm code in Serdia 2010 diagnostic system
B07 Electrical components
Engine alarm:
fuel pressure

## Slide 40
Oil pressure sensor
Oil pressure sensor
Pin measured to test sensor |  |  |  | 
ECU 52 | ECU 56b | X 17 | Sensor | Function
D2.1.21 | D2.1.24 | 23 | 1 | Power feed (5 VDC)
D2.1.72 | D2.1.44 | 26 | 2 | Signal
D2.1.35 | D2.1.57 | 27 | 4 | Ground
2
4
1
3
B08. Testing sensors

## Slide 41
The engine will start in this state.
Example alarm produced by disconnecting engine oil pressure sensor.
Alarm code on Infocenter / WOD:
Alarm code in Serdia 2010 diagnostic system
B07 Electrical components
Engine alarm:
Oil pressure

## Slide 42
Crankshaft speed sensor
Camshaft speed sensor | 
Engine off (0 rpm) | Frequency
 | 0 Hz
Idle speed (800 rpm) | Approx. 800 Hz
Mid speed (1,600 rpm) | Approx. 1.60 KHz
Rated speed (2,100 rpm) | Approx. 2.1 KHz
Pin measured to test sensor |  |  |  | 
ECU cv52 | ECU cv56 | X 17 | Sensor | Function
D2.1.75 | D2.1. | 1 | 3 | Shielding
D2.1.102 | D2.1. | 21 | 2 | Ground
D2.1.101 | D2.1. | 15 | 1 | Signal
1.6.
1.6.
Signal indicating crankshaft position with pistons 1 and 6 at TDC
B08. Testing sensors

## Slide 43
The engine will start in this state, but after a delay.
Example alarm produced by disconnecting crankshaft speed sensor.
Alarm code on Infocenter / WOD:
Alarm code in Serdia 2010 diagnostic system
B07 Electrical components
Engine alarm:
SPN 190 FMI 12

## Slide 44
Camshaft speed sensor
Crankshaft speed sensor | 
Engine off (0 rpm) | Frequency
 | 0 Hz
Idle speed (800 rpm) | Approx. 47 Hz (6 cyl.) Approx. 33 Hz (4 cyl.)
Mid speed (1,600 rpm) | Approx. 94 Hz (6 cyl.) Approx. 67 Hz (4 cyl.)
Rated speed (2 100 rpm) | Approx. 123 Hz (6 cyl.) Approx. 88 Hz (4 cyl.)
Pin measured to test sensor |  |  |  | 
ECU cv52 | ECU cv56 | X 17 | Sensor | Function
D2.1.99 | D2.1. | 13 | 1 | Signal
D2.1.100 | D2.1. | 14 | 2 | Ground
D2.1.75 | D2.1. | 9 | 3 | Shielding
Signal indicating camshaft position with piston 1 at TDC at end of compression stroke
1
5
3
6
2
4
4
1
5
B08. Testing sensors

## Slide 45
The engine will start in this state.
Example alarm produced by disconnecting camshaft speed sensor.
Alarm code in Serdia 2010 diagnostic system
B07 Electrical components
Alarm code on Infocenter / WOD:
Engine alarm:
SPN 190 FMI 12

## Slide 46
Rail pressure sensor
The rail pressure sensor.
Pin measured to test sensor |  |  |  | 
ECU cv52 | ECU cv56 | X 17 | Sensor | Function
D2.1.36 | D2.1.25 | 31 | 1 | Power feed (5 VDC)
D2.1.78 | D2.1.26 | 25 | 2 | Signal
D2.1.17 | D2.1.07 | 32 | 3 | Ground
Chart: 
| 0 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400 | 1500 | 1600 | 1700 | 1800 | 1900 | 2000 | 2100 | 2200 | 2300 | 2400
 | 0.5 | 0.72222 | 0.94444 | 1.1667 | 1.3889 | 1.6111 | 1.8333 | 2.0556 | 2.2778 | 2.5 | 2.7222 | 2.9444 | 3.1667 | 3.3889 | 3.6111 | 3.8333 | 4.0556 | 4.2778 | 4.5 | 4.5 | 4.5 | 4.5 | 4.5 | 4.5 | 4.5
 | 0.3 | 0.42273 | 0.54545 | 0.66818 | 0.79091 | 0.91364 | 1.0364 | 1.1591 | 1.2818 | 1.4045 | 1.5273 | 1.65 | 1.7727 | 1.8955 | 2.0182 | 2.1409 | 2.2636 | 2.3864 | 2.5091 | 2.6318 | 2.7545 | 2.8773 | 3 | 3 | 3
0.3
V
bar
2,200 Bar sensor
CRSN 3.3, 2,000 Bar
1,800 Bar sensor
CRSN 2, 1,600 Bar
Correlation between pressure / voltage
B08. Testing sensors
Sensor torque: 70 Nm
Torque for pressure cut-off valve: 110 Nm

## Slide 47
The engine will start in this state.
B07 Electrical components
Example alarm produced by disconnecting Rail sensor
Alarm code in Serdia 2010 diagnostic system
Alarm code on Infocenter / WOD:
Engine alarm:
SPN 157 FMI 3

## Slide 48
Voltage measurement (at zero engine load) |  | 
PIN | Ignition switch position | Voltage
Between 1 and 2 | Ignition on, engine off | 1.8 VDC - 0 VDC
 | Engine running at idle speed | 4.3 VDC
Pin measured to test FCU |  |  |  | 
EDC cv52 | EDC cv56b | PIN on socket X 17 | PIN on FCU | Function
D2.1.25 | D2.2.5 | 20 | 1 | Power
D2.1.46 | D2.2.4 | 19 | 2 | Ground
Measuring FCU resistance |  |  |  | 
Pin measured | PIN | Value | Condition | Note
Resistance in ohms | 1 - 2 | 3.6 OHM | 20 °C | Tolerance +/- 15%
FCU valve
B08. Testing sensors

## Slide 49
The engine will start in this state.
Example alarm produced by disconnecting proportional FCU solenoid valve installed on fuel control unit.
Alarm code in Serdia 2010 diagnostic system
B07 Electrical components
Alarm code on Infocenter / WOD:
Engine alarm:
SPN 523615 FMI 5

## Slide 50
Turbocharger with wastegate controlled by BusCan
Wastegate aperture controlled by engine ECU.
The wastegate is closed when the connector is disconnected.
Pin measured to test wastegate |  |  |  |  | 
EDC cv52 (ECU) | EDC cv52 (socket X17) | EDC cv56b (ECU) | EDC cv56b (socket X17) | PIN on wastegate | Function
 | 2.1 |  | 1.5 | 1 | Power feed from KENG and FY25 relays
 | 2.34 |  | 1.4 | 2 | Ground
D2.1.98 | 2.23 | D2.1.53 | 1.18 | 3 | Can L
D2.1.77 | 2.22 | D2.1.75 | 1.11 | 4 | Can H
KENG relay (21) located close to battery compartment (right hand side of tractor)
B08. Testing sensors