## Slide 1
24” LCD Display
Operating Temperature: -20°C to +60°C
EMI Mesh with Optical Bonding
700 nits Brightness
EMI/EMC Is Designed to Meet MIL-STD-461E/F
Shock Is Designed to Meet MIL-STD-810D
Vibration Is Designed to Meet MIL-STD-810E
Appearance
Features
24” Rugged Display with EMI Mesh & Optical Bonding
Rev. 0.1
ACT POWER TAIWAN
Preliminary
MIC-D2416

## Slide 2
Revision Table
Date | Revision | Content | By
2025/9/23 | 0.1 | First Draft | Zoe You
Rev. 0.1
MIC-D2416
24” Rugged Display with EMI Mesh & Optical Bonding
ACT POWER TAIWAN
Preliminary

## Slide 3
LCD Panel | 
LCD Size | 24-inch TFT
Backlight | LED
Resolution | 1920 x 1080
Interface | LVDS
View Angle | ± 89° (H), ±89° (V)
Luminance | 700 nits (after Bonding)
Contrast Ratio | 1000:1
Aspect Ratio | 16:10
Response Time | 14 ms
No. of Color | 1.07 B
Active Area | 518.4 (H) x 324 (V) mm
Pixel Pitch | 0.270 (H) x 0.270 (V)
LED Life time | 50,000 Hrs
EMI Mesh | Yes
Optical Bonding | Yes
Specification
Rev. 0.1
MIC-D2416
24” Rugged Display with EMI Mesh & Optical Bonding
ACT POWER TAIWAN
Preliminary

## Slide 4
ACT POWER TAIWAN
Preliminary
AD Board | 
Support VGA Signal | Color: 24 bit / Hor. Frequency: 30-80KHz / Ver. Frequency: 50-75Hz
Support DVI/HDMI Signal | Color: 24 bit / Hor. Frequency: 30-80KHz / Ver. Frequency: 50-75Hz
Input Interface | VGA / DVI / HDMI (1.3/1.4) / USB / Audio
Output Interface | 41-Pin / 0.5 mm LVDS Connector / Wafer 4-Pin 2.0 mm (R/L x1) AV Output x 1
Key Control | Power, Menu, Select, CH+, CH-, Up, Down
OSD Language | English
DC Input | DC +12V
Panel Select | DC +3.3V / +5V / +12V
Specification
Rev. 0.1
Environment Compliance
Operating Temp. | -20°C to +60°C
Storage Temp. | -30°C to +70°C
Humidity | Ta=40°C, 95%RH, Non-Condensing
Shock | Design to Meet MIL-STD-810D
Vibration | Design to Meet MIL-STD-810E
EMI/EMC | Design to Meet MIL-STD461E/F
Environmental performance may vary according to the integration method or final integration scenario.
MIC-D2416
24” Rugged Display with EMI Mesh & Optical Bonding

## Slide 5
Deliverables
1 | 24” Rugged Display with EMI Mesh & Optical Bonding
2 | AD Board
3 | LVDS Cable
4 | Convert Board
5 | Convert Board to AD Board Cable
6 | Backlight Cable
Ordering Information
Model Name | Description | Unit
MIC-D2416 | 24” Rugged Display with EMI Mesh & Optical Bonding | 1
Rev. 0.1
This datasheet is for informational purposes only and does not constitute professional advice, a contractual obligation, or a guarantee of any kind. While efforts have been made to ensure accuracy, ACT POWER TAIWAN makes no representations or warranties, express or implied, regarding its completeness or reliability. ACT POWER TAIWAN reserves the right to update, modify, or withdraw this document at any time without prior notice. Users should verify the suitability of the product for their specific application through independent testing and validation.
ACT POWER TAIWAN shall not be liable for any direct, indirect, or consequential damages arising from the use of this document.
Disclaimer
MIC-D2416
24” Rugged Display with EMI Mesh & Optical Bonding
ACT POWER TAIWAN
Preliminary