## Slide 1
Presented By: Bob Perry, Fleet Aftersales Manager
BASIC ELECTRICAL TROUBLESHOOTING & DIAGNOSTICS
Understanding the Electrical System of the 2024 Kenworth T480
Notes: Welcome! Today we’ll cover the basics of the Kenworth T480’s 12-volt electrical system — where to find key components, how to identify common issues, and what steps to take before calling for service.

## Slide 2
12-VOLT ELECTRICAL SYSTEM OVERVIEW
Powers starting, lighting, and accessories.
Supplied by batteries and the alternator.
Protected by fuses and relays.
Ground returns complete the circuit.
Notes: Think of electricity like water pressure — it flows through wires and components. Good connections and clean grounds keep that flow steady and prevent voltage drops.

## Slide 3
MAIN ELECTRICAL COMPONENTS
Battery: Stores 12V power.
Starter Motor: Cranks the engine.
Alternator: Recharges the batteries.
Power Distribution Center (PDC): Houses fuses and relays.
Ground Straps: Complete the return path for all circuits.
Notes: All these parts must work together. A loose cable, corroded terminal, or weak battery can affect several systems at once.

## Slide 4
FUSE & RELAY LOCATIONS
Under hood Power Distribution Center (PDC): on driver firewall/fender.
Cab Fuse Panel: below the driver’s dash.
Notes: These are your first stop when something quits working. Most electrical problems start with a blown fuse or poor connection here.

## Slide 5
STARTING SYSTEM POWER FLOW
Battery
Ignition Switch
Starter Relay
Starter Motor
Engine Crank
Notes: When you turn the key, voltage passes through a relay to the starter motor. If any link in that path is open, the engine won’t crank. Always start your checks at the battery and work forward.

## Slide 6
COMMON STARTING PROBLEMS
SYMPTOM | LIKELY CAUSE | QUICK CHECK
No crank / no click | Weak or dead batteries | Verify >12.4V; tighten terminals
Click, no start | Bad relay or poor ground | Check relay, inspect ground strap
Slow crank | Corroded cables or weak battery | Clean and tighten connections
No dash power | Blown fuse | Inspect cab fuse panel
Notes: Most starting issues come from battery or connection problems. Always rule those out first — they’re fast, simple fixes.

## Slide 7
LIGHTING SYSTEM OVERVIEW
Circuits include headlights, markers, brake & turn, dash lights.
Controlled by switches and relays.
Protected by fuses and grounded to the frame.
Notes: Lighting issues are often simple — blown fuse, bad bulb, or poor connection. Always check the ground before replacing parts.

## Slide 8
COMMON LIGHTING PROBLEMS
SYMPTOM | LIKELY CAUSE | QUICK CHECK
Headlight out | Burned bulb or blown fuse | Replace bulb or check fuse
Marker lights out | Corroded ground | Clean and reattach connection
Dash lights dim | Low voltage | Check alternator output
Turn signals erratic | Loose connector | Inspect plug pins
Notes: If multiple lights fail at once, suspect a shared ground or connector. Start at the simplest points — the fuse or the ground.

## Slide 9
SWITCHES & CONTROLS
Common switches: Headlight, Engine Brake, Fan, PTO.
Each sends a low-voltage signal to a relay.
Relay completes the circuit to operate the component.
Notes: Switches rarely fail on their own. If several stop working, look for a single power feed or shared fuse behind the dash.

## Slide 10
ELECTRICAL SYSTEM CARE
Keep terminals clean and tight.
Inspect cables for corrosion.
Check fuse panels for moisture.
Use dielectric grease on connectors.
Avoid accessory overload.

## Slide 11: STAY POWERED. STAY RELIABLE.
Know your fuses and cables.
Start simple with every issue.
Preventive care saves downtime.
Notes: Clean connections prevent 90% of electrical issues. A little preventive care goes a long way.

## Slide 12: SCENARIO #1: TRUCK WON’T CRANK AFTER SITTING OVERNIGHT
Driver turns key → no crank, no click.
Interior lights appear dim.
Batteries were last inspected 3 months ago.
What’s the FIRST thing you check?
What do dim lights usually tell you?
Notes: This is the most common real-world complaint. Dim lights are a giveaway that voltage is low. Encourage drivers to check battery connections and voltage before assuming the starter is bad.

## Slide 13: SCENARIO #1 SOLUTION: NO-CRANK CONDITION
Likely Causes:
Weak or drained batteries
Loose terminals
Corroded cable ends
Faulty starter relay
Correct Response:
Check battery voltage (>12.4V).
Inspect terminals (tight, clean).
Check for corrosion at ground strap.
Notes: The key message: start with the simple, visible checks before assuming expensive components have failed.

## Slide 14: SCENARIO #2: LIGHTS FLICKERING WHILE DRIVING
Driver notices headlights dimming and brightening.
Marker lights flicker on bumps.
No related dash warnings.
What is the most likely cause?
Fuse? Bulb? Connector? cable?
Notes: This is almost always a loose connection issue. Drivers should be trained to suspect loose connections before replacing bulbs.

## Slide 15: SCENARIO #2 SOLUTION: FLICKERING LIGHTS
Likely Cause:
Loose or corroded cable
Pin-fit issues in harness connectors
Correct Response:
Inspect connector near affected light circuit.
Clean and tighten connection.
Verify fuse seating in cab panel.
Notes: Flickering almost never comes from fuses. Grounds and connectors are the real culprits

## Slide 16: Quick Review: Question #1
What are the first two things you should check during ANY electrical problem?
Notes: read symptoms, not guess parts.

## Slide 17: Quick Review: Question #1
ANSWER:
Clean and tighten connection.
Verify fuse seating in cab panel.
What are the first two things you should check during ANY electrical problem?
Notes: golden rule: fuses and grounds fix the majority of electrical complaints.

## Slide 18: Quick Review Question #2
A truck clicks when the key is turned but does not start. What does this usually mean?

## Slide 19: Quick Review Question #2
A truck clicks when the key is turned but does not start. What does this usually mean?
ANSWER:
Weak battery and loose connections.

## Slide 20: REAL-WORLD EXAMPLE: CORRODED GROUND STRAP
Battery cable appeared “okay” from above.
Underside was fully corroded.
Caused intermittent no-start and lighting issues.
Notes: Many issues hide under cable insulation or behind the bolt surface. Inspection matters

## Slide 21: REAL-WORLD EXAMPLE: MISDIAGNOSED STARTER FAILURE
Truck towed in for “bad starter.”
Actual problem: battery negative cable loose.
Repair cost: $0.
Downtime: Completely avoidable.
Notes: .

## Slide 22: KNOWLEDGE CHECK (FINAL REVIEW)
Where is the cab fuse panel located?
What’s the normal battery voltage?
What causes flickering lights?
What’s the first thing to inspect in a no-start?

## Slide 23: KNOWLEDGE CHECK (FINAL REVIEW)
Where is the cab fuse panel located?
What’s the normal battery voltage?
What causes flickering lights?
What’s the first thing to inspect in a no-start?
Answers
Under dash drivers' side near left foot
>12.4 volts
Loose connector near headlight
Loose or corroded battery cable

## Slide 24: THANK YOU!
Notes: Understanding the basics gives you confidence to handle small problems before they become big ones. Thanks for learning today!