## Slide 1
Product Maintenance
Presented by: Moe Alkholany
Technical Solutions Support Specialist
Bendix Tech Team

## Slide 2
Product Overview
PuraGuard® Oil Coalescing Cartridge
Bendix® unique positioning of the oil coalescing media before the desiccant improves long term drying performance
Notes: How does the process work, emphasizing the technology used Bendix (Not all Oil Coalescing systems are the same)

## Slide 3
Product Overview
PuraGuard’s unique construction places the oil coalescing media before the desiccant bed which improves long-term drying performance. The coalescing filter consists of 17 layers of filter media and is placed in a vertical orientation which uses gravity to help remove oil droplets
PuraGuard® Oil Coalescing Cartridge
Notes: Bendix advanced technology, is a pre-desiccant filter using a special threated media

## Slide 4
PuraGuard® Oil Coalescing Cartridge
Effects of No or Low-Quality Oil Coalescing
Ref: Eaton Bulletin #TAIB-1006

## Slide 7
AD-HF air dryers are sold as SC (Service New with Core Charge)Purge Valve & Heater are common with the AD-IS®
Delivery Check Valve (DCV) is the same as used on the AD-9si®
4 Pressure Protection Valve (PPV‘s) kits currently released (based on pressure settings)
New 41mm cartridge PN: 5009041PG
Aftermarket Service Parts
K160650SC and K164018SC are Standard Purge Air Dryers
K160648SC and K160649SC are Extended Purge Air Dryers
4 Pressure Protection Valve (PPV) kits are released –same price
Notes: Parts Review

## Slide 8
Total Air Guarantee – T.A.G
Notes: Another Reason why to maintain you vehicle with all Genuine Bendix Parts

## Slide 9
  Pushrod home position. (Brakes released)
  Pushrod free stroke.
  Applied stroke length. (Power stroke)
  Lining material thickness & condition.
  Seized or damaged components.
  Excessive play in any components.
  Always remember that an ABA is only as good as it is installed and maintained.
Things to check for during an inspection.

## Slide 10
Bendix Versajust Automatic Slack Adjusters

## Slide 11
Brake Adjustment & Inspection involves all components from the chamber to the drum!
Chamber & Bracket
Pushrod
Clevis & Bushing
Spider & Anchor
Cam, Rollers & Bushings
Bracket, tube, bushings & Seals
Brake shoes & Springs
Brake Friction & Brake Drum
Slack Adjustment
Notes: Instructor: See Bw-7258 or BRSM-0033 ES & EB Service Manual – page # 14
Part number is located on the concave side of the cam lobes.
Head, splines and journals are heat treated as per OEM requirements.

## Slide 12
Inspect Slack Adjuster Bushing For Wear
Notes: One source of stroke problems is worn out clevis pins
Remember a brake system is a system of levels a fulcrums, each one of them must be in good working order for the system to work well
Ware at any one of the points will increase the overall stroke at the push rod and decrease the performance of the brake system

## Slide 13
Inspect Camshaft Bushing
Notes: Worn camshaft bushings will cause improper and premature lining wear. Previous slide is and indication of worn camshaft bushings and improper axial end play.

## Slide 14
Worn Camshaft Bearing Surface

## Slide 15
Old Hardware & Fatigued Springs
Notes: Old hardware and fatigued springs need to be replaced.

## Slide 16
Inspecting Brake Shoes.

## Slide 17
B2Bendix.com
  The one-stop shop for all your Bendix needs

## Slide 18
How to Search
Main Landing Page…
Site Search Bar… with Visual Search
Landing Page Navigation Bar…

## Slide 19
Select from the Products, Cross-References, Documents, and Software Tabs
Organizing Search Results

## Slide 20
Filter Search Results on the Product List Page (PLP) by technical product Information
Search Using Facets (Filters)

## Slide 21
  Over 25,000 Parts to search with more thank than 10,000 product images and 360° spins
  Detailed technical data & supporting documents
  Displays related service and replacement products
  Document library
  Compare feature
  Cross-Reference search
Product Information Available

## Slide 22
Information on the Product Detail Page:
Product Detail Page (PDP) content:
Related Service Items
General Part Information
Technical Attributes
Documents / Videos

## Slide 23
  Check Product Warranty Eligibility
From the Warranty Landing Page

## Slide 24
Support Information
Under Service & Support Header
Notes: Service Support Resource – Tech Team

## Slide 25
Available Marketing Collateral
SD-08-12046 Service Data for AD-HF® and AD-HFi®
S-1669_US_000 AD-HF Installation Instructions
S-1342_US-006 Cartridge Installation
BW8210 AD-HF Sell Sheet
AD-HF Rev 1 (10/2020) PowerPoint Overview
YouTube Videos
Introduction to the AD-HF
Servicing the AD-HF Air Dryer
Spin-On Cartridge Identification
Notes: Replaceable PPV, unlike AD-IS replace whole dryer. This is a ‘rebuildable’ Dryer

## Slide 26
B2Bendix.com (Products, service and support, e-learning, warranty, cores)
Brake-school.com (video-based products and system training)
Bendix in-person and virtual product schools, schedule on Bendix.com > BW2297
Bendix Knowledge-dock.com (blogs, tech tips, podcasts, position papers)
Bendix YouTube channel (Tech Talks, Driving With Videos)
In-person product demos (see your Bendix account manager)
Technician support & resources

## Slide 28
Bendix Contact Account Rep | Information
Kent Klausing Regional Field Sales – NW Account Manager Rihm KW | Phone #: 651-280-0069 Kent.Klausing@Bendix.com
Jason Hutchison Regional Field Sales – NE Account Manager RedBox | Phone #: 440-225-1944 Jason.Hutchison@Bendix.com
Moe Alkholany Technical Support Tech Team | TechTeam@Bendix.com 800-AIR-BRAKE (800-247-2725)
Questions