## Slide 1
DOT Requirements: Theory & Regulations
A Classroom Guide to Vehicle Inspections, Safety, and Compliance

## Slide 2
Why Inspections are Mandatory
Driver & Public Safety: The primary goal is to ensure the vehicle is safe to operate.
Legal Compliance: Required by law under FMCSR § 392.7 (Pre-Trip) and § 396.11 (Post-Trip).
Prevent Breakdowns: Identify and fix minor issues before they become major, costly repairs.
Avoid Violations: Proactively find and fix issues that would lead to fines or Out-of-Service (OOS) orders.

## Slide 3
By Weight
The vehicle has a gross vehicle weight rating (GVWR) or gross combination weight rating (GCWR) of 10,001 pounds or more.
Passengers (For-Hire)
Designed to transport more than 8 passengers (including the driver) for compensation.
Passengers (Private)
Designed to transport more than 15 passengers (including the driver), not for compensation.
By Material
Transports Hazardous Materials (HazMat) in a quantity requiring placarding, regardless of vehicle size.
What is a Commercial Motor Vehicle (CMV)?
A vehicle is subject to DOT/FMCSA regulations (driver qualification, maintenance, etc.) if it meets any of these criteria in commerce:

## Slide 4
Level I: North American Standard Inspection The most comprehensive. A full check of the driver (logs, license, med card) and a detailed vehicle inspection, including components underneath the truck.
Level II: Walk-Around Driver/Vehicle Inspection Includes all driver checks from Level I, but the vehicle inspection is a "walk-around" that doesn't involve getting under the vehicle.
Level III: Driver-Only Inspection Focuses entirely on the driver's credentials: HOS logs, CDL, medical certificate, and other required paperwork. No vehicle inspection is performed.
Level IV: Special Inspection A one-time, limited inspection to examine a specific feature (e.g., brakes, a recall item) or to gather data for a study.
Level V: Vehicle-Only Inspection An inspection of the vehicle (with no driver present) that can be performed at the carrier's location, a terminal, or roadside.
The Main 5 Levels of DOT Inspection

## Slide 5
What the Carrier & Driver Must Do (General)
Carrier Responsibilities :
Under § 396.3(a): The motor carrier must systematically inspect, repair, and maintain – or cause to be systematically inspected, repaired, and maintained.
The motor carrier must repair any defects or deficiencies noted by the driver on the DVIR, or certify that immediate repair is not necessary,
Driver Responsibilities :
Before operating the vehicle: complete a pre-trip inspection (visual & functional checks) Use the 7-point walk-around, and should review previous report.
At end of shift/day: complete (if required) a post-trip inspection report per § 396.11

## Slide 7
The "Walk-Around"
•
General: Look for leaks, damage, and vehicle stance.
•
Front: Lights, steering components, engine fluids, belts, hoses.
•
Sides: Tires (tread, pressure, cuts), wheels (lugs, seals), suspension (springs, U-bolts).
•
Rear: Lights, reflectors, coupling (fifth wheel, pintle), doors, splash guards.
Pre-Trip Inspection (§ 392.7)

## Slide 8
In-Cab & Brakes
•
In-Cab: Seatbelt, mirrors, horn, wipers, fire extinguisher, warning triangles.
•
Brakes: Test air brakes (check for air loss, low-pressure warning, and compressor cut-out).
•
Paperwork: Review the *previous* DVIR. If defects were noted, ensure a signed certification of repair is present *before* operating.
Pre-Trip Inspection (§ 392.7)

## Slide 9
Service & Parking Brakes
Lighting Devices & Reflectors
Tires, Wheels & Rims
CORE INSPECTION CHECKLIST

## Slide 10
Purpose: To identify any defects that developed during the day's operation.
Process: A thorough walk-around, similar to the pre-trip, checking all key safety components.
The Key: This is the inspection that is formally documented on the DVIR (if defects are found for trucks, or always for buses).
This report allows the motor carrier to schedule and complete repairs *before* the vehicle is dispatched for its next trip.
Post-Trip Inspection (§ 396.11)

## Slide 11
What is it? A formal written report completed by the driver at the end of each workday to document the vehicle's condition.
Property-Carrying: A DVIR must be submitted only if a safety-related defect is found or reported.
Passenger-Carrying: A DVIR must be submitted every day, even if no defects are found.
Driver's Signature: The driver must sign the report to certify that the inspection was
completed.
The Driver Vehicle Inspection Report (DVIR) (§ 396.11)

## Slide 12
ANNUAL DOT INSPECTION

## Slide 13
Federal law (49 CFR 396.17) mandates that every commercial vehicle must undergo an inspection at least once every 12 months.
COMPLIANCE REQUIREMENT
QUALIFIED INSPECTOR
Inspections must be performed by a qualified individual who understands FMCSA regulations and can identify defective components. This can be a 3rd party shop or a certified internal mechanic.

## Slide 14
Brakes
An OOS order is issued if 20% or more of a vehicle's service brakes are defective.
Tires
Tire failures can be catastrophic, especially on a steer axle.
•
Brakes out of adjustment
•
Audible air leaks
•
Oil-soaked brake lining
•
Cracked or broken drums
•
Steer Tires: Less than 4/32" tread depth.
•
Other Tires: Less than 2/32" tread depth.
•
Audible air leak.
•
Deep cuts exposing cord or belts.
•
Sidewall bulges.
Critical OOS Violations: Brakes & Tires

## Slide 17
Lights
Inoperative required lights, such as headlights, brake lights, tail lamps, or turn signals.
Cargo Securement
Failure to secure a load, insufficient tie-downs, or improper blocking and bracing.
Driver
Operating without a valid CDL, an expired medical certificate, or a violation of Hours of Service (HOS) rules.
More Critical OOS Violations

## Slide 18
For the Driver (In-Cab)
For the Vehicle (In-Cab)
For the Company (At Office)
Valid License (CDL/Chauffeur's)
Medical Examiner's Certificate
Record of Duty Status (HOS/ELD)
pre-trip/post-trip inspection reports (DVIRs)
Valid Registration (Cab Card / IRP)
Proof of Liability Insurance
Proof of Annual Inspection
IFTA License & Decals (if interstate)
Driver Qualification Files (DQF)
Drug & Alcohol Program Records
Full Maintenance & Repair History
Proof of UCR & Operating Authority
Accident Register
DOT Documentation: Who, What, Where?
Required documents are split between the driver, the vehicle, and the company's home office.

## Slide 19
Record Type | Retention Period
Driver Qualification File | Employment + 3 years after
Drug & Alcohol (positive/refusal) | 5 years
Drug & Alcohol (negative) | 1 year
Hours of Service (logs/ELD) | 6 months
Vehicle Maintenance Records | 1 year + 6 months post-sale
Annual Inspection | 14 months
DVIR | 3 months
Accident Register | 3 years
🚛 Record Retention Requirements (FMCSA)

## Slide 20: Key Onboard Safety Equipment (Required by FMCSA/DOT):
Fire Extinguisher:
  5 B:C / 10 B:C
  Must be properly charged, mounted securely.
Warning Devices (for Stopped Vehicles):
  Three Bi-Directional Emergency Reflective Triangles.
  Must be ready for immediate use to warn approaching traffic if the vehicle stops on the roadside.
  Alternative Three liquid-burning flares.

## Slide 21
specifically DOT C2 tape, is mandatory for commercial trailers over 80 inches wide with a gross vehicle weight over 10,000 pounds to enhance visibility. This tape must be alternating red and white segments, and placement requires covering at least 50% of each side, the entire lower rear bar, and an inverted "L" shape on the top rear corners
Required reflective tape (§ 393.11)

## Slide 22
Thank you for your attention.