## Slide 2: Bale Bed Hydraulic System Comparisons
Pumps & power sources
Valve types & functions
Bale bed cylinder force
Bale bed lift capacity (calculated & advertised)

## Slide 3: The Original Bed Hydraulic Power
In 1979, truck PTO hydraulic power seemed the only logical choice for the original unit.

## Slide 4: 1979-1981 Proving Ground: PTO-Driven Pump
Quickly discovered that hay bale loading, feeding & unrolling was a totally different operation than dumping & lowering a grain box once every few hours.
Was always stopping, shifting transmission to neutral, re-engaging clutch to get hydraulic power
Decided to research 12-volt hydraulics

## Slide 5: 1979-1981 Research Results: 12-volt Hydraulic Systems
They were commonly used on delivery truck lift-gates & 5th wheel grain trailers
We questioned owners of 12-volt hay handlers & found that many were fed up with the problems.
In 1980, a significant number of those cattlemen intended to switch to clutch pump systems as soon as possible

## Slide 6: 1979-1981 Research Results: 12-volt Hydraulic Systems
The common problems were:
  Corrosion
  Wiring fires
  Dead batteries with no warranty
Another key reason mentioned to avoid 12-volt hydraulics was the frustratingly slow speed, especially in cold weather when the majority of feeding occurs

## Slide 7: Comparison:
Final pump selection came as a result of practical comparison of features and capabilities
Gear Pump from typical 12-volt hydraulic system
Gear Pump used in Hydra Bed
12-Volt vs. Clutch Pump

## Slide 8
Typical 12-Volt pump inlet port diameter is 0.500”
Clutch pump inlet port is 1.000”
Our choice: Clutch Pump
Hydraulic Pump Inlet Port Diameter
.500”
1.000”

## Slide 9
Typical 12-Volt pump pressure port diameter is 0.300”
Clutch pump pressure port is .750”
Our choice: Clutch Pump
Hydraulic Pump Pressure Port Diameter
.300”
.750”

## Slide 10
Input shaft diameter & overall pump dimensions
7/8” shaft, key & taper drive
1/2” shaft, tang drive
Our Choice:
Clutch Pump
Pump Drive Shaft and Overall Dimensions

## Slide 11
Electric starter motor drive
Hydraulic Pump Drive System
Belt-drive from truck’s engine
Our Choice:
Live Engine Power

## Slide 12
Battery power, 15 feet of cable & several high-amp connections that are eventually likely to corrode?
Hydraulic Pump What Power Source?
Our Choice:
Belt Drive
Simple, Proven V-Belt Drive

## Slide 13: 12-Volt Hydraulics: Battery Life
In 1980, 12-Volt hydraulic system owners often stated: “My local battery retailer told me he was sorry, but he just couldn’t sell me any more batteries with warranty!”
Our Decision:
Too much hassle!

## Slide 14: 12-Volt Hydraulics: Charging System Challenges
12-volt hydraulic systems create significant additional load on alternator
All power must still be produced by the engine
Our Decision:
Alternators already have enough load!

## Slide 15: 12-Volt Hydraulics: Switches & Solenoids
Each bale handler motion requires the control switches & solenoids to connect and hold an electrical load
Our Decision:
We’ve don’t need the complexity or the vulnerability!

## Slide 16: 12-Volt Hydraulics: Repair Costs
During a recent winter season, these failed 12-volt motors & pumps were replaced at the bed owner’s expense by the dealer. No photo is available of the large number of additional units that were replaced under manufacturer’s warranty. Photo courtesy: The Arc Shop - Exeter, MO
Replacement 12-Volt control switch: $6.00
Replacement 12-Volt motor solenoid: $12.00
Replacement truck battery: $60.00
Replacement 12-Volt pump drive motor: $250.00
Equipment Down-Time: Costly & Frustrating!
Clutch Pump Dependability: Priceless!
Our Decision:
The dependability of the clutch pump hydraulic system!

## Slide 17: Are 12-Volt hydraulic systems a good choice for some applications?
Lift gates on delivery trucks? Yes, due to single action function, low duty cycle & low oil flow requirements
Bale spikes & spike beds? Yes, due to low duty cycle & oil volume requirements and single circuit function
Bolt-down bale handlers for low volume operations? Yes with special provisions for increased current supply

## Slide 18: Typical 12-Volt Hydraulic Pump Output Flow Declines as Pressure Increases
PSI 500 1,000 1,500 2,000 2,500
GPM
Pump output is reduced by half at 2,500 PSI

## Slide 19: Typical 12-Volt Hydraulic Pump Amp Draw Increases as Pressure Increases
PSI 500 1,000 1,500 2,000 2,500
Amps
Current Draw doubles from 500 to 2,500 PSI
Acceptable Current Draw for Vehicle Starter
Excessive Current - Starter Life & Output Reduced

## Slide 20: ALL 12-Volt Hydraulic Pumps: Unfortunately, as hydraulic demand increases, pump performance decreases
PSI 500 1,000 1,500 2,000 2,500
GPM
Amp Draw

## Slide 21: Hydraulic Power Systems: Is Triple C “Up to speed” on 12-Volt Hydraulics?
We build a top-quality 12-Volt hydraulic system for our BD-2200 Bolt Down unit

## Slide 22: Hydraulic Power Systems: Why don’t we provide Hydra Beds with 12-Volt Hydraulic systems?
Hydra Bed hydraulic systems are expected to provide fast, dependable bale loading during every season of the year.

## Slide 23: Hydraulic Power Systems Considerations:
In the heat of feeding or haying season, the last thing anyone wants is trouble with hydraulics.
?

## Slide 24: Hydraulic Power Systems: Solution: Clutch Pump & Manual Valve
We believe our customers deserve only the best in Hydra Bed hydraulics!
Our History:
Powerful, Simple, Dependable Hydraulics for 20 years!

## Slide 25: Have 12-volt hydraulic systems changed significantly in 23 years?
In 1980, 12-volt hydraulic pump systems were comprised of the following components:
  Small displacement, throw-away gear pump
  Brush-type, 12-volt starter motor drive
  Small capacity (typically less than 1 gallon) oil reservoir

## Slide 26: How does that compare to today’s 12-volt hydraulic pumping system?
Today, 12-volt hydraulic pump systems are typically comprised of the following components:
  Small displacement, throw-away gear pump
  Brush-type, 12-volt starter motor drive
  Small capacity (typically less than 1 gallon) oil reservoir
  Some now equipped with plastic reservoirs
  Some motors now utilize bearings instead of bushings

## Slide 27: What about other 12-volt drive motor types?
Permanent magnet motors are now appearing on certain 12-volt hydraulic pumps.
These motors eliminate brush & commutator wear and maintenance, BUT:
  They still suffer the basic power limitations of traditional 12-volt hydraulic systems
  Duty cycle is still very limited, especially at high output pressures
  Flows still decline as pressures increase

## Slide 28: What factors limit 12-volt hydraulic pumping system improvements?
Typical 12-Volt pumping system requires 250 amps (4.0 Horsepower) of electrical power to produce 2,500 PSI
At that 2,500 PSI pressure, the system can only deliver 1.3 GPM
At a 250 amp load, the pump can only be run 27 seconds, then, to avoid damage to the motor, MUST be allowed to cool for at least 4-1/2 minutes before being run again
ALL 12-volt hydraulic pumping systems possess similar duty cycle limitations

## Slide 29: How does Hydra Bed clutch pump performance compare to 12-volt systems?
The Hydra Bed clutch pump generates 11 GPM @ 2,000 RPM @ 2,500 PSI
At that 2,500 PSI pressure & 11 GPM flow, the pump is utilizing approximately 17 horsepower from the truck engine
The Hydra Bed clutch pump is generating more than 5 times the hydraulic power and has no limits on duty cycle

## Slide 30: What does this all mean to the owner of a 12-volt powered bale bed?
12-volt pumping systems on bale beds are routinely abused by duty cycle requirements BEYOND their recommended capacity
While these pumping units will typically not fail immediately from this abuse, their life span is shortened by EVERY such occurrence
It is not uncommon for heavy users of 12-volt bale beds to replace motors and/or pumps as frequently as once a year, often at their own expense
Unfortunately, replacing these expensive components is only a temporary solution to the problem

## Slide 31: Bale Bed Hydraulics: Control System Complexity
12-volt bale beds use as many as 3 function switches in addition to 1 or 2 micro switches.
The Hydra Bed uses 1 toggle switch to engage the clutch pump & 2 sealed cables to operate the valve.
As the quantity & fragility of control components increase, so does the potential for problems.
Our Goal:
Simplicity & dependability!

## Slide 32: Bale Bed Hydraulics: Troubleshooting Issues
It’s a cold, snowy day in December. Your good customer’s bale bed isn’t working, and he’s got 300 cows that haven’t been fed yet. Where do you start troubleshooting this complex control system?

## Slide 33: The “Pliers & Baling Wire” approach to ranch equipment maintenance!
Many Hydra Bed owners are too busy caring for their stock to have time to work on equipment!

## Slide 34: The “I can do anything that can be done from a saddle!” approach
These good operators are usually much better stockmen than they are mechanics!

## Slide 35: The “Not Mechanical!” approach
Some are just not comfortable doing mechanical work. These customers will often tell you that they are often better off NOT working on their equipment!

## Slide 36: The approach
Few (if any) sensitive and/or fragile components used in equipment design & construction
Products developed & intended to excel under the normal abuse of ranch life
Simple diagnostic & repair procedures
Easy access to all key components

## Slide 37: Bale Bed Hydraulics: Valve “Feathering” Capability
Like a tractor front loader, a bale bed is used for many unique lifting & loading tasks
Our Choice:
Fully-variable manual controls!
In a tractor loader system, good valve metering is critical. On-Off solenoid valves just aren’t capable of providing the variable flow control necessary for smooth, safe operation of load handling equipment.

## Slide 38: Bale Bed Hydraulics: Valve Load Checks
Load Checks are integral to the design of Hydra Bed manual control valves, and have been for 20 years
This key feature prevents unwanted load movement during spool shifting
Our Choice:
Load check-equipped manual valves for 20 years!

## Slide 39: Hydraulics: Control Valve Summary
Simplicity
Ruggedness
Dependability
Excellent metering
Superior control of fast-moving, heavy loads
Our Choice:
Trouble-Free manual valves for 20 years!

## Slide 40: Hydraulic Systems Dependable Clutch Pump & Manual Valve!
Our Committment:
Powerful, Simple, Dependable Hydraulics for over 20 years!

## Slide 41: Bale Bed Hydraulic Systems: Calculating Cylinder Force
The mathematic formula for calculating Hydraulic Cylinder Force is very simple:
Inside Area - Shaft Area x System Pressure
Pounds/Square Inch
The result will be expressed in pounds. For systems with dual cylinders, multiply by 2. Dividing by 2,000 gives force in Tons.
-
x

## Slide 42: Lift Cylinder Effective Area
Total Effective Lifting Area 14.1 Square Inches
Inside Diameter 4-1/2”
Shaft Diameter 1-1/2”
System Pressure 2,500 PSI
Total Force Generated 17.6 Tons

## Slide 43: Lift Cylinder Effective Area
Total Effective Lifting Area 14.1 Square Inches
Inside Diameter 4-1/2”
Shaft Diameter 1-1/2”
System Pressure 2,200 PSI
Total Force Generated 15.9 Tons
DewEze®

## Slide 44: Lift Cylinder Effective Area
Total Effective Lifting Area 10.8 Square Inches
Inside Diameter 4”
Shaft Diameter 1-1/2”
System Pressure 2,250 PSI
Total Force Generated 12.2 Tons
Steerman™

## Slide 45: Lift Cylinder Effective Area
Total Effective Lifting Area 10.8 Square Inches
Inside Diameter 4”
Shaft Diameter 1-1/2”
System Pressure 2,500 PSI
Total Force Generated 13.5 Tons
Krogmann™

## Slide 46: Lift Cylinder Effective Area
Total Effective Lifting Area per Cylinder 5.8 Square Inches Times 2 Cylinders = 11.6
Inside Diameter 3”
Shaft Diameter 1-1/4”
System Pressure 2,000 PSI
Total Force Generated 11.6 Tons
Hoswel™
Dual Lift Cylinders

## Slide 47: Lift Cylinder Effective Area
Total Effective Lifting Area per Cylinder 5.8 Square Inches Times 2 Cylinders = 11.6
Inside Diameter 3”
Shaft Diameter 1-1/4”
System Pressure 2,500 PSI
Total Force Generated 14.5 Tons
Besler™
Dual Lift Cylinders

## Slide 48: Lift Cylinder Effective Area
Total Effective Lifting Area per Cylinder 5.8 Square Inches Times 2 Cylinders = 11.6
Inside Diameter 3”
Shaft Diameter 1-1/4”
System Pressure 2,250 PSI
Total Force Generated 13.1 Tons
Cannonball™
Dual Lift Cylinders

## Slide 49: Important Background Information
Lift cylinder force calculations were made using industry-standard hydraulic formulas
All cylinder dimensions and system relief pressure values are from product advertising or were provided by representatives of the various companies
Cylinder force values are compared in the next table
The final table compares estimated lift capacities based on the calculated cylinder force values
Every effort has been made to provide accurate, unbiased information in these comparisons
We reserve the right to make additions or corrections as additional information becomes available

## Slide 50: Bale Bed Hydraulic Systems: Comparing Cylinder Force
DewEze 15.9 Tons 90% of Hydra Bed
Besler 14.5 Tons 82% of Hydra Bed
Krogmann 13.5 Tons 77% of Hydra Bed
Cannonball 13.1 Tons 74% of Hydra Bed
Steerman 12.2 Tons 69% of Hydra Bed
Hoswel 11.6 Tons 66% of Hydra Bed
17.6 Tons - The Leader

## Slide 51: Simple Bale Bed Facts:
Fact: Cylinder force (area times pressure) is a key factor in comparing true bale bed lift capacity
Fact: All listed bale beds use similar lift cylinder strokes, ranging from DewEze at 16” to all others at 20”
Fact: All listed bale beds convert that cylinder stroke to a similar bale arm swing radius
Fact: The lift cylinder in a Hydra Bed will produce 17.6 Tons of force at the factory system relief pressure of 2,500 PSI
Fact: That 17.6 Tons of force will lift 3,000# at the spinner bushing of a Series 150 Hydra Bed
Fact: Advertised lift capacities should reflect true lift capacities

## Slide 52: Advertised Lift Capacity compared to Calculated Lift Capacity
DewEze 2,750# 2,700# -50# -2%
Besler 2,200# 2,460# +260# +11%
Krogmann 2,750# 2,310# -440# -19%
Cannonball 2,850# 2,220# -630# -28%
Steerman 2,850# 2,270# -580# -26%
Hoswel 2,500# 1,980# -520# -26%
3,000# 3,000# 0# 0%
Advertised Lift Capacity
Lift Capacity Calculated from Cylinder Force
Estimated Discrepancy