## Slide 1
Southern Significant Event Fast Facts – Staff working open line on ACR Canterbury West vice FDM
Note: This document contains information understood to date (72hrs post incident) and information may change following investigation
On the 10th of May 2026, a three-person Ultrasonic team were working in a possession on the FDM within an X worksite. The team were dealing with train suspects and rail defects that required testing and had already covered several locations, working their way along the ELR. The setup included one designated driver and a two-person team on track.
After leaving Canterbury East, the team made their way to their next planned access point at Tonford ‘B’ (FDM 60m 12ch, PICOP land). While on route, the COSS contacted the PICOP as expected.
The team mistakenly accessed Tonford on the ACR at 60m 68ch instead. After accessing the line and walking around 1–2 chains, they saw a train approaching and moved into the safe cess. Once there, they realised the approaching train was a passenger service. Approximately 15–20 seconds later, the train passed.
At this point, the team recognised they had accessed the wrong ELR. They safely exited via the cess and reported the incident to their Line Manager.
Initial cause identified:
Confusion over the access point contributed to the incident, as both locations share similar names and local terminology is used on both the ACR and FDM ELRs.
The team did not use access point signage or any other checks to confirm their location before accessing the track, relying instead on their familiarity with Tonford crossing on the ACR.
In this area, the ACR and FDM run parallel to each other, and both have access points that include the name ‘Tonford’, which increased the potential for confusion.
Immediate actions taken:
Statements collected from NR staff.
For cause screening carried out
Changes made to names of access points in the National Hazard Directory
Key issues for the investigation to consider:
How was the planning of the work undertaken and how was the access point chosen ?
Did the use of a designated driver, combined with contacting the PICOP while en route and then proceeding directly onto track upon arrival, reduce the opportunity for the team to pause and carry out a “Take 5” to confirm their exact location prior to accessing the line ?
Could this happen in other locations: Yes
DCP: Dave Bonner
Level of investigation: Level 1
SE REF: 00045106