## Slide 1
Vibration Suppression Technology A Functional Classification Framework for Drilling Dysfunction Mitigation
Chris Marland
Chevron
June 18, 2026
Based on SPE-230712-MS Chris Marland - Chevron
Naveen Nair – Halliburton
Lotfi Hamoudi – Halliburton
Guy Feasey – Neo Oiltools
Paul Pastusek – Pastusek & Associates

## Slide 2: Vibration – Understanding and Definition Growth
Axial Vibration
Bit Bounce
Torsional Vibration
Stick-Slip
Forward Whirl
Lateral Vibration
High-Frequency Axial Oscillation (HFAO)
High-Frequency Torsional Oscillation (HFTO)
Reverse Whirl
Notes: Over time our understanding of drilling dysfunction has increased. From axial vibration, torsional and lateral we’ve since developed a greater definition of each mode of dysfunction. That definition doesn’t just cover the direction of movement, but thanks to high-frequency measurement devices we can define this movement as a function of frequency – how many times per cycle does the BHA move in a particular way.

## Slide 3: Bit, BHA Design & Mitigation Technologies
System Design
Bit Design
Stabilizer Position & Design
BHA Size & Length
DrillPipe Size
Drive Type
Operating Parameters
System Design
Bit Design
Stabilizer Position & Design
BHA Size & Length
DrillPipe Size
Drive Type
Operating Parameters
Vibration Suppression Systems
Vibration Suppression Systems
Notes: As understanding BHA dynamics expanded, it has provided additional opportunity insights that may inform system redesign discussions. Designs have changed to account for lateral stability, motors, RSS tools, fulcrum points, torsional stability and force balancing. BHA designs include not only stabilizer placement, but stabilizer designs on leading and trailing edges. There has also been a focus on the effects of operating parameters on dysfunction magnitude, and which has the biggest impact for mitigation. Another step in analysis, although perhaps not as well studied, is the effect of autodriller designs and operation on dysfunction and on mitigation.
Over the last 20 years or more downhole technologies have been developed to try to deal with dysfunction. Initially there may have only be a single tool for each mode, such as shock subs for axial vibration, but more recently the number of technologies has increased significantly. Some of those come from the expansion of the unconventional market volume, some from patent expiration and some from a desire to help protect BHA components to retain market share and keep costs down. I think we have seen that by the development of tools from major directional drilling OEMs and not just from smaller independents.

## Slide 4
Axial Dampeners, Shocks Subs & Agitation
Lateral Stability & Isolation
Torsional Suppression & Dampening
Notes: So, what has happened? From early development of shock subs and other axial dampers the technologies designed to mitigate vibration have expanded.
Initially these focused on discrete modes of vibration, axial vibration dampening, lateral stability and torsional suppression, initially of stick-slip. Over time technologies developed to include agitation as a friction reducer then various forms of torsional tools to deal with stick-slip and HFTO and more recently torsional dampeners that convert torsional energy rather than dampening it.
What has also occurred is that tools are being marketed to address multiple modes of vibration. While it is simple to describe a mode of vibration, torsional or axial for example, that doesn’t explain the differences each mechanism presents, the frequency of oscillation for example. It also doesn’t define how one mode may trigger another, axial being triggered by torsional and how the frequency of the main dysfunction affects the frequency of another.
Tool design can be a significant factor influencing how effective a technology is at mitigating vibration. One of the biggest factors being internal friction, especially in mechanical tools. When we consider what a tool is designed to do compared to what it is marketed to do, there is a need to separate the primary benefits from the secondary benefits. For example, a tool designed to mitigate lateral vibration that benefits secondary axial as the BHA flexes, may be marketed as benefiting both. But would that same tool work if the vibration encountered was purely axial?
A method is needed to classify technology by primary design features and assess a technology, even qualitatively against other similar technologies to determine what works best for an application.
The paper we have written aims to provide that guidance and classification. We’ve also included guidance on how to evaluate problems as they occur, through forensics and diagnostics so that engineers can engage in informed technical discussions with tool providers as appropriate. It may be helpful if tool manufacturers provide more detail how tools function, primary vs secondary mitigation capabilities and perhaps even begin to evaluate their own designs and any internal friction or design elements that may affect capability.

## Slide 5: Classification Table
Notes: This is the classification table we are proposing for guidance.
The first column separates vibration into the three defined modes and their mechanisms. It is important for engineers & directional companies to correctly identify the mechanism(s) that are present in their application. There is guidance in the paper on what measurements to make and forensic analysis to conduct that can help with this definition. When we define vibration here it is about the primary mode or mechanism. More often that not, mitigating that, mitigates secondary effects. This framework attempts to conceptually describe potential impacts of downhole tools on the primary vibration.
Gamma Ray is used as a proxy for formation type. We know this isn’t definitive and you may have more refinements available to you, but it is good practice to understand geological influence. If GR is used, the API values quoted are not fixed and should be application specific. For example, if your sub-surface team want to use 75api or 60 api as a high/low GR cut-over, that’s fine.
Application type defines the broad application wellbore design where vibration is present. Again, these are not necessarily designed to be fixed. If you drill 45-degree tangents where vibration differs from a lateral application, then define that for your business. Wellbore inclination & curvature influence both vibration mechanisms and the capabilities of some technologies. It needs to be factored into the evaluation, especially if you hole section of concern crosses these broad categories.
We also include a method for indicating if a technology actively affects depth of cut. This is predominately a feature of some torsional vibration tools, but not all. Understanding that, and even measuring that a with high-frequency measurement sub can help quantify tool performance. You can use this to determine if those tools affect ROP positively or negatively. There may be a perception that DoC management may reduce ROP, but field evidence suggests that is may contribute to more stable dynamics and potentially an improvement in bit efficiency and therefore ROP, although results may vary by application.
Across the top we’ve subdivided the types of technologies by their external movement design and broadly how they have been designed internally. As you can see, some tools have additional definition for high & low friction. This should be determined through field trials and evaluation of vibration response. The paper gives some guidance on conducting field trials, what to keep, what to change, what to measure and how, and some guidance on procedures. It is important to test and evaluate. The first tool you try might reduce vibration compared to no-tool so you may determine its effectiveness compared to nothing. Subsequent tools may perform differently, which could prompt re-evaluation.
This framework is intended only as a conceptual guide and should be adapted case-by-case. There is evidence out there that some downhole technologies work better with some bit types, geology, application, hole size, fluid type etc. Use the document as guidance when moving to a new development area or even a new geographical area.
We also hope that tool designers look at this as an opportunity to better classify their tool and explain what the primary intent of the tool is and what secondary benefits it may bring if those are needed. ROP isn’t a consideration here. ROP will be supported by reliability improvement and dysfunction reduction outside of any redesign efforts.
Mention of specific technologies or tool categories is for technical illustration only and does not imply endorsement or preference for any vendor, manufacturer, or commercial product.
Performance outcomes may vary depending on application, formation, and operational factors. No guarantee of performance is implied

## Slide 6: Classification Table
Notes: This is the classification table we are proposing for guidance.
The first column separates vibration into the three defined modes and their mechanisms. It is important for engineers & directional companies to correctly identify the mechanism(s) that are present in their application. There is guidance in the paper on what measurements to make and forensic analysis to conduct that can help with this definition. When we define vibration here it is about the primary mode or mechanism. More often that not, mitigating that, mitigates secondary effects. This framework attempts to conceptually describe potential impacts of downhole tools on the primary vibration.
Gamma Ray is used as a proxy for formation type. We know this isn’t definitive and you may have more refinements available to you, but it is good practice to understand geological influence. If GR is used, the API values quoted are not fixed and should be application specific. For example, if your sub-surface team want to use 75api or 60 api as a high/low GR cut-over, that’s fine.
Application type defines the broad application wellbore design where vibration is present. Again, these are not necessarily designed to be fixed. If you drill 45-degree tangents where vibration differs from a lateral application, then define that for your business. Wellbore inclination & curvature influence both vibration mechanisms and the capabilities of some technologies. It needs to be factored into the evaluation, especially if you hole section of concern crosses these broad categories.
We also include a method for indicating if a technology actively affects depth of cut. This is predominately a feature of some torsional vibration tools, but not all. Understanding that, and even measuring that a with high-frequency measurement sub can help quantify tool performance. You can use this to determine if those tools affect ROP positively or negatively. There may be a perception that DoC management may reduce ROP, but field evidence suggests that is may contribute to more stable dynamics and potentially an improvement in bit efficiency and therefore ROP, although results may vary by application.
Across the top we’ve subdivided the types of technologies by their external movement design and broadly how they have been designed internally. As you can see, some tools have additional definition for high & low friction. This should be determined through field trials and evaluation of vibration response. The paper gives some guidance on conducting field trials, what to keep, what to change, what to measure and how, and some guidance on procedures. It is important to test and evaluate. The first tool you try might reduce vibration compared to no-tool so you may determine its effectiveness compared to nothing. Subsequent tools may perform differently, which could prompt re-evaluation.
This framework is intended only as a conceptual guide and should be adapted case-by-case. There is evidence out there that some downhole technologies work better with some bit types, geology, application, hole size, fluid type etc. Use the document as guidance when moving to a new development area or even a new geographical area.
We also hope that tool designers look at this as an opportunity to better classify their tool and explain what the primary intent of the tool is and what secondary benefits it may bring if those are needed. ROP isn’t a consideration here. ROP will be supported by reliability improvement and dysfunction reduction outside of any redesign efforts.
Mention of specific technologies or tool categories is for technical illustration only and does not imply endorsement or preference for any vendor, manufacturer, or commercial product.
Performance outcomes may vary depending on application, formation, and operational factors. No guarantee of performance is implied

## Slide 7: Testing – Adherence and Measurements
Test Plan
  Bit & BHA Design – Same as Offsets
Execution
Follow standard operating practices
  Baseline – 1 or 2 wells
Execute step tests
  Step Tests
  High-Frequency Measurement Subs
Post-Run Analysis
Time Based Analysis
Depth Based Analysis
Forensic Analysis
Notes: Rationale for keeping designs the same – limit changes to be a scientific as possible. Include comments on mud type, weight and flow rates, especially in a motorized system.
Baseline first 1 or 2 wells on pad, depending on number of wells. Use offsets, but focus on current pad to minimize uncertainty
Define steps tests that modify either WOB or RPM to determine what is most effective
High-Frequency measurement sub – why & benefits
Execution
  Drill as you do so you understand what you are doing. Detect an issues with back-to-bottom procedures, connection practices, pick-up amounts etc
  Execute step tests – that means defined buy-in from all stakeholders to do it properly and record them in daily reports for tracking
Post-Run Analysis
  Time-based – details of on bottom and off bottom dysfunction
  Depth-based – Influence of formation – especially at transitions
  Forensics – bit or BHA post-run conditions improved. Tear down changes including the mitigation tool. May take a few wells / pads to see a trend

## Slide 8: Sampling Rate, Duration, and Location Requirements Depend on the Signal(s) of Interest
To detect stick slip and bit bounce, the signals need to be sampled at 1-10 samples per second for a period of 20-30 seconds
Lateral vibrations need to be sampled within the BHA at 10 - 50 samples per second for a period of 20-30 seconds
HFTO and HFAO signals need to be sampled within the BHA, below the motor, at 1000-2000 samples per second for a period of 2-3 sec minimum
Notes: Sampling ranges are illustrative and may vary by tool manufacturer and application.

## Slide 9: Post-Run Evaluation Examples
Notes: Explain a review and comparison of overall vibration levels against drilling parameters. Overall mitigation and comparison at different loads and perhaps even founder point identification.
Explain the need to review and compare the same data on a depth basis with a formation identifier. Vibration may change with formation change which may help direct operating parameters as formation changes
Detailed time breakdown to look at formation transitions. Transitions can create high transient vibration that only a downhole tool can mitigate. Focus on mitigation effect at formation boundaries to determine effectiveness.
The technologies, tools, and methods described may not perform uniformly across all geologies, well designs, or operational environments. Any references to performance improvements are illustrative and do not constitute a guarantee, warranty, or representation of specific operational outcomes.

## Slide 10: Thank You
Chris Marland | Chevron
Vibration Suppression Technology – A Functional Classification
Framework for Drilling Dysfunction Mitigation C. Marland, V.N. Nair, L. Hamoudi, G. Feasey, & P. Pastusek
SPE 230713-MS
Notes: This document is intended for technical discussion only and does not establish any the companies engineering practices, standards, or operating procedures.