## Slide 1
The following presentation was given at the 2026 IADD Downhole Tool Series Extended Luncheon focused on
Vibration Suppression Technology
June 18th, 2026
The Woodlands, Texas All Rights Reserved
https://www.iadd-intl.org/2026-downhole-tool-series-presentations

## Slide 2
Notes: Good afternoon,
My name is Wes Heiskell – Director of Paradigm Drilling and Intervention.

## Slide 3: Drilling TOOL kit
Located in the drill string just behind the drill bit, the DRIVER reduces frictional vibrations and creates favourable weight conditions on the drill bit
The DRIVER enhances in the horizontal drilling performance
Hydraulically drill-fluid activated. The EXTREAMER tool expands to increase hole size while drilling ahead or after a drilled pilot hole
Drill wells frequently show micro doglegs and other wall profile imperfections
The REAMER contains no moving parts and delivers drill string stabilisation and passive hole gauging in one tool diamond faced tool
Drilling cuttings agglomeration creates problems in horizontal drilling with drilling mud flow, cuttings size and drill string torque
The REBEL tools enhance the removal of drilling cuttings enhancing horizontal drillings performance
Bending of rotating drill strings creates additional torque and drag in horizontal drilling operations.
Multiple RUNNER subs are tactically positioned in drill string to significantly reduce this negative friction to rolling bearing support
Notes: Today I’ll discuss how the Paradigm Driver addresses some of the biggest drilling challenges we face, reducing downhole shock and vibration, and improving weight transfer to the bit.
Alongside the Driver, our portfolio includes the Exteamer, Reamer/Stabilizer, Rebel, and Runner - all designed to boost efficiency and reduce mechanical risk.

## Slide 4
Notes: Now, focusing on the Driver – with a quick video
The Driver has been run in RSS applications placed above the motor to maximize energy transfer to the lower string, which improves ROP while maintaining less WOB, and reduces stick-slip, shock, vibration, and pipe buckling - extending tool life and improving overall drilling performance.

## Slide 5
Notes: The Driver acts like a downhole tractor. Two rollers are always engaged with the wellbore while the remaining rollers keep the tool centered and moving smoothly. As the drillstring rotates, the rollers engage in sequence, creating a continuous crawling motion.
The 15-degree angled traction pads convert side-load forces into forward thrust, helping pull the lower drillstring out of buckling, improve weight transfer to the bit, and reduce vibration for more efficient drilling, and longer bit life with BHA reliability.

## Slide 6: 6 ¾” MWD Shock - depth
Higher MWD shock on offset run than Driver run.
OFFSET WELL
Notes: In the U.S., the Driver is on its 7th trials, with 4 more planned, using Pason, MWD, and RSS data to gather the results:
On this slide from a super major job, 6-1/8” hole in the Delaware Basin - the offset well axial vibration spiked from 60 Gs down to 10, and lateral vibration spikes were well over 100+ Gs to about 15.
With the Driver, axial vibration remained steadily range of 14–15 Gs, while lateral vibration ranged from 30 Gs to15 Gs.- the results show a much smoother, more stable drilling operation
Overall, we’re seeing 60–80% less vibration on all trials, 15–20% lower WOB for the same ROP, and up to 30% longer bit life.

## Slide 7: 6 ¾” Weight transfer – end of run
Offset run – Up to 10klbs weight loss between upper and lower tool
Driver run – no separation in weight between upper and lower tool – superior weight transfer
DRIVER WELL
Weight on bit (klbs)
Weight on bit (klbs)
OFFSET WELL
Notes: This slide shows the offset well surface weight applied is spiking from 30 to 35 – the light and dark blue lines are the upper and lower censer subs – showing the wide spikes from surface weight to the bit – some case there's 35 surface, upper sub 20 and low as 10.
The Driver had more of a consistent weight transfer to the bit – 30 to 35 at surface and 25 to 30 to 35 at the bit censer sub tracing green and orange – true bit tracking driven by 1,250–3,000 lbs of effective axial thrust recorded from the censer subs, with minimal separation versus the offset. The Driver is pulling the lower string out of buckling and dampening slick slip

## Slide 8: DRIVER® Summary dashboard – major Delaware basin
Key Results from Trial Runs
  Improved Drilling Performance: +10–15% higher ROP with consistent weight transfer and zero downtime
  Lower WOB Required: Achieved comparable ROP using 15–20% less weight on bit
  Reduced Vibration Risk: Stick-slip, axial vibration, and shock events reduced to <2% (vs. ~20% offsets) — 60 - 80% + reduction
  Extended Bit Life: No major cutter damage; full runs with zero unplanned trips
  Stable drilling Performance: Smooth, consistent logs vs. erratic offset wells
Operational Impact vs. Offset Wells
  Faster Drilling: 0.3–0.5 days saved per section ($175K–$200K savings)
  Reduced NPT: 16–19 hours saved from lower vibration → better energy transfer, improved bit life, fewer repair costs
  Eliminated Extra Trips: Avoided at least one round trip due to improved tool performance
Bottom Line
  Smoother drilling, lower risk, and significant cost savings.
Key Results With Paradigm Driver®
Notes: So, what did we see?
We delivered 10–15% higher ROP while using 15–20% less WOB, confirming more efficient weight transfer to the bit.
Vibration performance improved dramatically, with stick-slip, shock, and axial vibration reduced by over 60 to 80% compared to offset wells.
The result was smoother drilling, improved bit life, zero unplanned trips, and time savings per well.
Bottom line: better drilling performance, lower risk, and meaningful cost savings.

## Slide 9
COMBINE DOWNHOLE TRACTION WITH TORQUE REDUCTION
Converts 30-50% of collar side force into traction
Skewed rollers help pull upper BHA into tension
Next generation of weight transmission technology
Unlocks drilling parameters for improved ROP & significantly reduced stick slip
Notes: I have a Driver here - outside. Come-on by. Thank you!

## Slide 10
The preceding presentation was given at the 2026 IADD Downhole Tool Series Extended Luncheon focused on
Vibration Suppression Technology
June 18th, 2026
The Woodlands, Texas All Rights Reserved
https://www.iadd-intl.org/2026-downhole-tool-series-presentations